## Slide 1: Symbolic Logic Optimization and Encoding
Giovanni De Micheli
Integrated Systems Laboratory
This presentation can be used for non-commercial purposes as long as this note and the copyright footers are not removed
© Giovanni De Micheli – All rights reserved

## Slide 2: Outline
Symbolic minimization
Encoding problems:
  Input encoding
  Output encoding
  Mixed encoding
Notes: We consider extensions to two-level logic optimization to cope with problems where the choice of the representation of the inputs and/or outputs is free.
This problem is relevant for the design of interconnected logic blocks as well as for the encoding of finite-state machines.

## Slide 3: Symbolic minimization
Minimize tables of symbols rather than binary tables
  Extension to bvi and mvi function minimization
Applications:
  Simplification of tables of symbols
  Simplification of interconnected logic blocks
  Encoding of finite-state machines
Notes: The minimization of Boolean functions where the codes of the inputs and/or outputs are not specified is referred to as symbolic minimization.
It is tightly related to multiple-valued logic optimization, and indeed it coincides with minimization of mvi-functions in some particular cases.
There are 3 interesting subproblems, called input, output and mixed encoding respectively.

## Slide 4: Example (input encoding)
INSTRUCTION DECODER
ad-mode
op-code
control
Notes: Consider an instruction decoder.
It has two input and one output fields, related the the addressing mode (ad-mode), operation code (op-code) and control, respectively.

## Slide 5: Example
ad-mode op-code control
INDEX AND CNTA
INDEX OR CNTA
INDEX JMP CNTA
INDEX ADD CNTA
DIR AND CNTB
DIR OR CNTB
DIR JMP CNTC
DIR ADD CNTC
IND AND CNTB
IND OR CNTD
IND JMP CNTD
IND ADD CNTC
Notes: This table shows the behavior of the decoder.
The ad-mode can take one of the three symbolic inputs {INDEX, DIR, IND} (that are mnemonics for indexed, direct and indirect addressing);
the op-code can indicate one of the four instructions:{AND, OR, JMP, ADD };
the output corresponds to one of four control signals { CNTA, CNTB, CNTC, CNTD }.
The general problem is then to replace the symbols by binary strings, so that the corresponding minimum cover is minimum over all codes.

## Slide 6: Definitions
Symbolic cover:
  List of symbolic implicants
  List of rows of a table
Symbolic implicant:
  Conjunction of symbolic literals
Symbolic literals:
  Simple: one symbol
  Compound: the disjunction of some symbols
INDEX AND CNTA
INDEX OR CNTA
INDEX JMP CNTA
INDEX ADD CNTA
DIR AND CNTB
DIR OR CNTB
DIR JMP CNTC
DIR ADD CNTC
IND AND CNTB
IND OR CNTD
IND JMP CNTD
IND ADD CNTC
Notes: A symbolic cover is a generalization of a Boolean cover.
It is a table, whose rows are symbolic implicants.
Each implicant shows the conjunction of symbolic literals.
Since symbolic literals are multi-valued, there are two cases:
A literal has one value (simple)
A literal has more than one value (compound)

## Slide 7: Input encoding problem Rationale
Degrees of freedom in encoding the symbols
Goal:
  Reduce size of the representation
Approach:
  Encode to minimize number of rows
  Encode to minimize number of bits
Notes: We concentrate our attention first on the encoding of the input fields of a symbolic table.
Thus we assume that the output codes are given.
Since we do not know the input codes, we cannot specify a bv-function that can be minimized.
Trying all possible input codes would be excessively costly, because it would require an exponential number of logic minimizations.
Fortunately, it is possible to optimize the function independently of the encoding, and determine the codes at a later time.
This requires performing the minimization at the symbolic level, before the encoding.

## Slide 8: Input encoding problem
Represent each string by 1-hot codes
Table with positional cube notation
Minimize table with mvi minimizer
Interpret minimized table:
  Compound mvi-literals
  Groups of symbols
Notes: For input encoding, a straightforward model for symbolic functions and their optimization is to consider them as mvi-functions and apply mvi-minimization.
The issue at hand is how to interpret the compound symbolic literals.

## Slide 9: Example
1000 1000
0100 1000
0010 1000
100 0001 1000
010 1000 0100
010 0100 0100
010 0010 0010
010 0001 0010
001 1000 0100
001 0100 0001
001 0010 0001
001 0001 0010
100 1111 1000
010 1100 0100
001 1000 0100
010 0011 0010
001 0010 0010
001 0110 0001
Encoded cover:
Minimum cover:
100
100
100
100
ad-mode
INDEX 100
DIR 010
IND 001
op-code
AND 1000
OR 0100
JMP 0010
ADD 0001
control
CNTA 1000
CNTB 0100
CNTC 0010
CNTD 0001
Notes: The example shows the mvi-cover for the instruction decoder and a minimum representation.

## Slide 10: Example
Minimum symbolic cover:
Examples of:
  Simple literal: AND
  Compound literal: AND, OR
INDEX AND,OR, JMP, ADD CNTA
DIR AND,OR CNTB
IND AND CNTB
DIR JMP, ADD CNTC
IND ADD CNTC
IND OR,JMP CNTD
Notes: Once the minimum mvi-cover is transformed back using the symbols, the equivalent symbolic cover shows the most compact behavior of the decoder.
In the example, the first implicant means that under ad-mode INDEX, any op-code (full literal) implies control CNTA.
The second implicant means that under ad-mode DIR, either op-code AND or OR imply control CNTB.
Both are examples of compound literals.

## Slide 11: Input encoding problem
Transform minimum symbolic cover into minimum bv-cover
Map symbolic implicants into bv implicants (one to one)
Compound literals:
  Encode corresponding symbols so that their supercube does not include other symbol codes
Replace encoded literals into cover
Notes: An important issue is the preservation of the cardinality of such a cover.
This can be achieved by searching for an encoding where each mvi-implicant is mapped into one bv-implicant.
Hence the encoding of the input symbols must be such that each mv-literal corresponds to only one cube in the binary-valued representation.
If a mv-literal has only one 1, then it can be mapped trivially into the cube representing the code of the corresponding symbol.
Difficulties arise when a mv-literal has more than one 1s, because the smallest single cube that is always true when the input matches any of the corresponding symbols is the supercube of their codes. Indeed, such a cube may cover other points of the Boolean space.
It is important that the supercube does not intersect the code of other symbols not in the literal, otherwise a spurious value may erroneously assert the function.
It is obvious that full literals do not create problems, because any input would make them \true. Hence they can be translated into the universal cube and pose no constraint on the encoding.

## Slide 12: Example
Compound literals:
  AND, OR, JMP, ADD (similar to don’t care)
  AND, OR
  JMP, ADD
  OR, JMP
X
Notes: In the picture on the left the codes are valid.
Indeed, the supercubes are 0*, 1* and *1 respectively.
In the picture on the right the codes are invalid.
Now, the supercubes corresponding to {AND,OR} and to {JMP,ADD} are both **, and intersect the other codes. T
his would cause any op-code to make that mv-literal true, erroneously.

## Slide 13: Example
Valid codes:
Replacement in cover:
AND 00
OR 01
JMP 11
ADD 10
1111
1100
1000
0011
0010
0110
**
0*
00
1*
10
*1
00 ** 1000
01 0* 0100
11 00 0100
01 1* 0010
11 10 0010
11 *1 0001
Final cover
Notes: Once the codes are chosen, they can be replaced in the cover.

## Slide 14: Input encoding algorithms
Problem specification:
  Constraint matrix A:
  ai j = 1 iff symbol j belongs to literal i
Solution sought for:
  Encoding matrix E:
    As many rows as the symbols
    Encoding length nb
Notes: The encoding problem can be modeled by a binary constraint matrix A, whose n_r rows are the field of the optimized cover corresponding to the symbol set S under consideration.
Note that full literals and literals with cardinality one can be dropped, because they do not represent encoding constraints.
The matrix has as many columns as the n_s symbols.
The codes of the symbols are represented by a binary matrix E, which is the unknown of the problem. Each row of E is the encoding of a symbol.
The code length n_b is also an unknown.

## Slide 15: Example
Constraint matrix:
Encoding matrix:
A =
1 1 0 0
0 0 1 1
0 1 1 0
0 0
0 1
1 1
1 0
E =
  AND OR JMP ADD
  AND OR JMP ADD
Compound literals:
  AND, OR, JMP, ADD = *
  AND, OR
  JMP, ADD
  OR, JMP
Notes: For the minimum cover of the instruction decoder example, there are the corresponding matrices.
Note that A specifies the problem, while E is the solution.

## Slide 16: Input encoding problem
Given constraint matrix A:
  Find encoding matix E satisfying all input encoding constraints (due to compound literals)
  With minimum number of columns (bits)
Notes: The optimum input encoding problem can be stated as this.
It is intractable.

## Slide 17: Dichotomy theory
Dichotomy:
  Two sets (L,R)
  Bipartition of a subset of the symbol set
Encoding:
  Set of columns of E
  Set of bipartitions of symbols set
Rationale:
  Each row of the constraint matrix implies some choice on the codes
Notes: Exact encoding algorithms have been proposed, that transform the encoding problem into a covering or a coloring problem.
They rely on the notion of dichotomy, that is a bipartition of a subset of the symbol set S.
The rationale is that any column of matrix E corresponds to a bipartition, induced by the assignment of bit 1 or bit 0 to each code.
An encoding matrix is then equivalent to a set of bipartitions.
To determine such a set, we need to consider the constraints and how they induce appropriate bipartitions.

## Slide 18: Dichotomies
Dichotomy associated with row aT of A:
  A set pair (L, R)
    L has the symbols with the 1s in aT
    R has the symbols with the Os in aT
Seed dichotomy associated with row aT of A:
  A set pair (L, R)
    L has the symbols with the 1s in aT
    R has one symbol with the O in aT
Notes: Dichotomies and seed dichotomies are defined above.
They can be derived from each row of matrix A, and they describe the constraints.

## Slide 19: Example
Dichotomy associated with constraint aT = 1100:
  ({AND, OR}; {JMP, ADD})
The corresponding seed dichotomies are:
  ({AND, OR}; {JMP})
  ({AND, OR}; {ADD})
Notes: The dichotomy is trivially derived from the row.
The seed dichotomies are derived by splitting the dichotomy, and they express the need that symbols JMP and ADD do not have a code intersecting the supercube of the encoding of symbols AND and OR.

## Slide 20: Definitions
Compatibility:
  (L1; R1) and (L2; R2) are compatible if:
    L1  R2 = Ø and R1  L2 = Ø
Covering:
  Dichotomy (L1; R1) covers (L2; R2) if:
    L1 ≥ L2 and R1 ≥ R2
Prime dichotomy:
  Dichotomy that is not covered by any compatible dichotomy of a given set
Notes: A few properties and operations can be defined over dichotomies.
Note that a dichotomy is compatible with the one obtained by exchanging the left and right blocks.
This symmetry is typical of the input encoding problem, and is related to the fact that valid encodings are preserved under column complementation.

## Slide 21: Extended definitions
Compatibility:
  (L1; R1) and (L2; R2) are compatible if:
    L1  R2 = Ø and R1  L2 = Ø
    or
    L1  L2 = Ø and R1  R2 = Ø
Covering:
  Dichotomy (L1; R1) covers (L2; R2) if:
    L1 ≥ L2 and R1 ≥ R2
    or
    L1 ≥ R2 and R1 ≥ L2
Prime dichotomy:
  Dichotomy that is not covered by any compatible dichotomy of a given set
Notes: A few properties and operations can be defined over dichotomies.
Note that a dichotomy is compatible with the one obtained by exchanging the left and right blocks.
This symmetry is typical of the input encoding problem, and is related to the fact that valid encodings are preserved under column complementation.

## Slide 22: Exact input encoding
Compute all prime dichotomies
Form a prime/seed table
Find minimum cover of seeds by primes
Notes: The set of prime dichotomies represent possible bipartitions (with maximal blocks) that are compatible with the constraints.
Only a subset of the prime dichotomies is necessary to satisfy the constraints.
Namely a subset that covers all seed dichotomies.
Hence the encoding problem can be cast as the search of all prime dichotomies that originate from a constraint matrix and as a minimum covering problem.

## Slide 23: Example
Seed dichotomies:
Primes dichotomies :
s1 ({AND, OR} ; {JMP})
s2 ({AND, OR} ; {ADD})
s3 ({JMP, ADD}; {AND})
s4 ({JMP, ADD}; {OR})
s5 ({OR,JMP} ; {AND})
s6 ({OR,JMP} ; {ADD})
p1 ({AND, OR} ; {JMP,ADD})
p2 ({OR,JMP} ; {AND,ADD})
p3 ({OR, JMP, ADD} ; {AND})
p4 ({AND, OR, JMP} ; {ADD})
Notes: This example shows all seed dichotomies (elementary constraints) and all primes.

## Slide 24: Example
Table:
Minimum cover : p1 and p2
Encoding:
1 0
1 1
0 1
0 0
E =
s1 s2 s3 s4 s5 s6
p1 1 1 1 1 0 0
p2 0 0 0 0 1 1
p3 0 0 1 0 1 0
p4 0 1 0 0 0 1
p1 ({AND, OR} ; {JMP,ADD})
p2 ({OR,JMP} ; {AND,ADD})
  AND OR JMP ADD
Notes: Given a prime dichotomy table, a set of primes that covers all seeds specifies a solution.
Namely the first two primes provide a minimum cover.
Now, we can obtain a solution E by taking t the two primes as columns for E, and by assigning a 1 to the left part entries and a 0 to the right parts.
Indeed we have created a partition of the symbol set that satisfies the constraints.

## Slide 25: Remarks
Satisfying all encoding constraints may require more than the minimum number of bits Log2 n for n symbols
1-hot encoding satisfies all possible constraint sets, but n bits are needed
Trade-off is possible between coding length and constraint satisfaction, that then relates to minimality of the cover

## Slide 26: Heuristic encoding
Determine dichotomies of rows of A
Column-based encoding:
  Construct E column by column
Iterate:
  Determine maximum compatible set of dichotomies
  Find a compatible encoding
  Use it as column of E
Notes: A heuristic algorithm is as follows.
It does not compute the seed nor the prime dichotomies.
It just uses the dichotomies associated with the rows of A.
At each step, maximal sets of compatible dichotomies are computed, and the one of largest cardinality is selected.
An encoding column satisfying this set of dichotomies is derived and appended to E.
The rationale of the algorithm is to satisfy as many constraints as possible in a greedy fashion.
Hence it does not guarantee the global minimality of the number of columns used.

## Slide 27: Example
Dichotomies
First two dichotomies are compatible
Encoding column 1100T satisfies d1, d2
Need to satisfy d3
Second encoding column 0110T
d1 ({AND, OR} ; {JMP,ADD})
d2 ({JMP,ADD} ; {AND,OR})
d3 ({OR, JMP} ; {AND,ADD})
1
1
0
0
E =
0
1
1
0
Notes: The first two dichotomies are compatible, and the corresponding constraints can be satisfied by the encoding column [1100].
The second column is chosen then to be [0110] to satisfy the remaining constraint.

## Slide 28: Output and mixed encoding
Output encoding:
  Determine encoding of output symbols
Mixed encoding:
  Determine both input and output encoding
  Examples
    Interconnected circuits
    Circuits with feedback
Notes: The output encoding problem consists of choosing codes for the outputs of a Boolean function that minimize the cardinality of its minimum cover.
Symbolic minimization is no more a straightforward application of mvi-minimization.
Indeed, the output codes play a significant role in reducing the size of a function.
The mixed encoding is a further generalization.

## Slide 29: Example
INSTRUCTION DECODER
ad-mode
op-code
control
Notes: In this example, you may assume to be free to choose the encoding of the output.

## Slide 30: Example
INSTRUCTION DECODER
ad-mode
op-code
SECOND STAGE
select
output
control
Notes: In this example, you may assume to be free to choose the encoding of the output of the first block, which is the input to the second block.
Then, such encoding must be chosen while considering an input and an output encoding problem at the second and first block respectively.
This is an example of mixed encoding.

## Slide 31: State encoding of finite-state machines
Given a state table of a finite-state machine:
  With symbols representing
    present-states
    next-states
Find a consistent encoding of the states:
  That minimizes the size of the cover
  With minimum number of bits
Notes: The finite-state machine encoding problem consists of determining an encoding of the states that minimize its size.
Let us assume that the FSM is implemented by two-level logic.
Hence, we want to encode the states (inputs) and next-states (outputs) to minimize the number of terms and while minimizing also coding length.

## Slide 32: Symbolic minimization
Extension to mvi-minimization
Accounts for:
  Covering relations
  Disjunctive relations
Exact and heuristic minimizers
Notes: When optimizing the symbolic table with mvi-minimizers, no implicant merging can take place while exploiting the implicant output-parts, because output symbols are viewed as independent of each other.
Indeed each output symbol is considered as an independent input in the positional cube notation.
Instead, when covering (and/or disjunctive) relations among outputs can be used, the cover cardinality can be further reduced.

## Slide 33: Example
Minimum symbolic cover computed before:
Can we use fewer implicants?
Can we merge implicants?
INDEX AND,OR, JMP, ADD CNTA
DIR AND, OR CNTB
IND AND CNTB
DIR JMP, ADD CNTC
IND ADD CNTC
IND OR, JMP CNTD
Notes: Consider again the instruction decoder table and let us look for opportunities to reduce the number of symbolic implicants to less than 6.

## Slide 34: Example
Merging implicants:
Conflict:
  Conditions for CNTD overlaps conditions for CNTB and CNTC
  Make sure CNTD overrides the others  bitwise cover
INDEX AND,OR, JMP, ADD CNTA
DIR AND, OR CNTB
IND AND CNTB
DIR JMP, ADD CNTC
IND ADD CNTC
IND OR, JMP CNTD
INDEX AND,OR, JMP, ADD CNTA
DIR, IND AND, OR CNTB
DIR,IND JMP, ADD CNTC
IND OR, JMP CNTD
Notes: Consider again the instruction decoder table and let us look for opportunities to reduce the number of symbolic implicants to less than 6.

## Slide 35: Example covering relations
Assume the code of CNTD covers the codes of CNTB and CNTC:
Possible codes:
  CNTA = 00, CNTB = 01, CNTC = 10 and CNTD = 11
100 1111 CNTA
001 1100 CNTB
011 0011 CNTC
001 0110 CNTD
Notes: Consider the instruction decoder.
The minimum cover could be reduced from six to four implicants, under the assumption that the code of CNTD covers the codes of CNTB and CNTC.
Note that the apparent conflict between the fourth and both the second and third implicants is resolved by the covering relation.
For example, the following codes could be used: CNTA = 00, CNTB = 01, CNTC = 10 and CNTD = 11.

## Slide 36: Example disjunctive relations
Assume the code of CNTD is the OR of the codes of CNTB and CNTC:
Possible codes:
  CNTA = 00, CNTB = 01, CNTC = 10 and CNTD = 11
100 1111 CNTA
010 1100 CNTB
010 0011 CNTC
001 0111 CNTB
001 0111 CNTC
Notes: As a second example, the corresponding table is achieved under the constraint that the code of CNTD is the OR (disjunction) of the codes for CNTB and CNTC.

## Slide 37: Output encoding algorithms
Often solved in conjunction with input encoding
Exact algorithms:
  Prime dichotomies compatible with output constraints
  Asymmetry: L not interchangeable with R
  Construct prime / seed table
  Solve covering problem
Heuristic algorithms:
  Construct E column by column
Notes: The output encoding problem requires solving first symbolic minimization and then an encoding problem.
In this case, as well as for solving the combined input and output encoding problems, symbolic minimization differs from multiple-valued logic minimization and is indeed a novel problem.
Symbolic minimization optimizes a cover while exploiting covering and disjunctive relations among codes, as described above.
In practice, the output encoding problem is often considered in conjunction with an input encoding problem.
For ouput/mixed encoding, there are two approaches:
Exact methods, based on computation of prime dichotomies and minimum cover computation.
Heuristic methods based on column-wise construction of matrix E.

## Slide 38: Example
Input constraint matrix of second stage:
Output constraint matrix of first stage:
Assume the code of CTND covers the codes of CTNB and CTNC
A =
1 1 0 0
0 1 0 1
B =
0 0 0 0
0 0 0 0
0 0 0 0
0 1 1 0
Notes: An output/mixed encoding problem is specified by two matrices
A for the input constraints (compound literals)
B for the covering relations
In this example, matrix B represents the fact that CNTD covers the codes of CNTB and CNTC.

## Slide 39: Example
Seed dichotomies associated with A:
Seed dichotomies s2 and s8 are not compatible with B
s1 ({CNTA, CNTB} ; {CNTC})
s2 ({CNTA, CNTB} ; {CNTD})
s3 ({CNTC} ; {CNTA, CNTB})
s4 ({CNTD} ; {CNTA, CNTB})
s5 ({CNTB, CNTD} ; {CNTA})
s6 ({CNTB, CNTD} ; {CNTC})
s7 ({CNTA} ; {CNTB, CNTD})
s8 ({CNTC} ; {CNTB, CNTD})
Notes: Starting from the seed dichotomies associated with matrix A, we remove those that are not compatible with matrix B.

## Slide 40: Example (2)
Prime dichotomies compatible with B:
Cover: p1 and p2
Encoding matrix
0 0
0 1
1 0
1 1
E =
p1 ({CNTC, CNTD} ; {CNTA, CNTB})
p2 ({CNTB, CNTD} ; {CNTA, CNTC})
p3 ({CNTA, CNTB, CNTD} ; {CNTC})
  AND OR JMP ADD
Notes: This example shows the prime dichotomies compatible with B, a minimum cover and the corresponding encoding matrix E.

## Slide 41: Example
Notes: Example of FSM with 5 states to encode.
Note that states need to be encoded consistently, I.e., the same symbol as present or next state must have the same code.

## Slide 42: Example
Minimum symbolic cover:
Covering constraints:
  s1 and s2 cover s3
  s5 is covered by all other states
Constraint and encoding matrices:
A =
1 1 0 1 0
0 0 0 1 1
B =
0 0 1 0 1
0 0 1 0 1
0 0 0 0 1
0 0 0 0 0
* s1 s2 s4 s3 0
1 s2 s1 1
0 s4 s5 s2 1
1 s3 s4 1
E =
1 1 1
1 0 1
0 0 1
1 0 0
0 0 0
Notes: This slide shows the minimum symbolic table fo the FSM.
It has 4 implicants.
It determines the encoding constraints, represented by matrices A and B.

## Slide 43: Example
Encoding matrix (one row per state):
Encoded cover of combinational component:
E =
1 1 1
1 0 1
0 0 1
1 0 0
0 0 0
* 1** 001 0
1 101 111 1
0 *00 101 1
1 001 100 1
Notes: This slide shows the final encoding matrix E, satisfying the constraints given by A and B.
It shows also the final Boolean cover for the FSM.

## Slide 44: Summary
Symbolic minimization:
  Reduce size of tabular representations where symbols in table can be encoded
Requires solving encoding problems:
  Find minimum-length encoding that is valid for a minimum symbolic cover
Applicable to optimizing:
  Interconnected combinational blocks
  Combinational part of finite-state machines
Notes: In summary, symbolic minimization and encoding are two steps for reducing the size of two-level representations.
This approach is useful for:
- Logic blocks with a freedom in deciding the signals’ representation,
- For interconnected logic blocks where the internal signal representation is irrelevant,
- And for finite-state machines.